## Slide 1
Towards Robust Methods for Indoor Localization using Interval Data
N. Ramdani, D. Zeinalipour-Yazti, M. Karamousadakis & A. Panayides
ALIAS @ IEEE MDM2019, Hong Kong, June 10th, 2019.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under the Marie Sklodowska-Curie grant agreement No 823887

## Slide 2
Motivation and Background

## Slide 3: Indoor Localization
People spend 80-90% of their time indoor. (USA Environmental Protection Agency 2011).
>85% of data and 70% of voice traffic originates from within buildings. (Nokia 2012).
Current trend are Internet-based Indoor Navigation (IIN) services, based on measurements collected by smart and Internet of Thing (IoT) enabled devices.

## Slide 4: Internet of Things data
Large variety of technologies & methods
Diverse quality performance
  Noisy WiFi RSS => Low accuracy & robustness
State-of-the-art solutions for improving consistency, and smoothing estimates:
  averaged signals
  advanced probabilistic models
  hybrid methods, sensor fusion
This talk investiguates bounded-error estimation.

## Slide 5
Bounded-error estimation

## Slide 6: Estimation
Classical estimation is probabilistic

## Slide 7: Bounded-error estimation
Unknown-but-bounded-error framework
Set Membership Algorithm

## Slide 8
Interval analysis & Constraint satisfaction problems.

## Slide 9: Interval Arithmetic
  (Dwyer,51) (Warmus,56) (Sunaga,58) (Moore,59), (Moore, 66), (Jaulin, et al. 01)

## Slide 10: Interval Arithmetic

## Slide 11: Interval Arithmetic
y = sin(x)
x
y
[x]
[y]

## Slide 12: Interval Arithmetic
(x-2)(x+3)

## Slide 13: Set Inversion
Set Inversion via Interval Analysis SIVIA (Jaulin et al., 93)
  Inclusion test. Branch-&-Prune. Branch-&-Bound

## Slide 14: Constraint Satisfaction Problems
F. Rossi, et al. (Eds.), Handbook of Constraint Programming, Elsevier, 2006.
L. Jaulin, et al., Applied Interval Analysis, Springer-Verlag, 2001

## Slide 15: Numerical Constraint Satisfaction Problems
Complexity. Solving numerical CSP is in theory NP-hard. Actual time complexity is generally tractable: successful applications in
  operation research, scheduling and planning, vehicle routing, component configuration, networks, and bioinformatics.
Interval & CSP solving toolboxes
  IBEX. (ibex-lib.org) (Chabert & Jaulin, 2009) C++ library for constraint processing over real numbers. …

## Slide 16
Bounded-error estimation in presence of data outliers

## Slide 17: Set-membership Estimation with outliers
q-Relaxed intersection

## Slide 18: Algorithm for q-Relaxed intersection (Jaulin, 2009)

## Slide 19
Infrastructure-Based Localisation Techniques with Interval Data

## Slide 20: Robust Localization
Example #1. Robot localisation via ToF-based Multilateration
  Can measure the distance to a beacon
  ToF. Time of Flight
  Bounded-error framework

## Slide 21: Robust Localization
TOF
1 beacon
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 22: Robust Localization
TOF
2 beacons
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 23: Robust Localization
TOF
4 beacons
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 24: Robust Localization
TOF
4 beacons
1 corrupted
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 25: Robust Localization
TOF
1-relaxed
Intersection
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 26: Robust Localization
TOF
1-relaxed
Intersection
Spurious datum identified
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 27: Robust Localization
Example #2. Robot localisation via TDoA Multilateration
  Can measure the distance difference to beacons
  TDoA. Time Difference of Arrival
  Bounded-error framework

## Slide 28: Robust Localization
TDoA
4 beacons
no corruption
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 29: Robust Localization
TDoA
4 beacons
1 faulty synchroniz.
3-relaxed intersection
Figures obtained using PYIBEX tool. benensta.github.io/pyIbex

## Slide 30
Infrastructure-Free Localization Techniques with Interval Data

## Slide 31: Interval Fingerprinting
Interval Radio-Map.

## Slide 32: WKNN & Fingerprints
v1
v2
Fingerprints in Radio Map
x
y
Corresponding locations
query
1
2
3
3NN

## Slide 33: WKNN & Interval Fingerprints
v1
v2
Interval Fingerprints in Radio Map
x
y
Corresponding locations
query
1
2
3NN
3

## Slide 34: Hausdorff distance
[b]
[a]
Explicit formulas for computing the Hausdorff distance using distances on bounds (Jahn 1990).

## Slide 35: Experimental Evaluation
Manhattan
Euclidian
Chebyshev
RMS error on GPS coordinates

## Slide 36
Concluding remarks

## Slide 37: Use of Interval Data…
for indoor localization, is effective.
with infrastructure-based techniques, provides uncertainty intervals for reconstructed positions.
with infrastructure-less techniques, interval fingerprinting provides smoother and more consistent localization estimates.
Future work will consider further experimental evaluation, and implementation into the Anyplace software.

## Slide 38
Thank you!