## Slide 1: Anyplace Indoor Information Service
Challenges of Fingerprinting in Indoor Positioning and Navigation
Department of Computer Science, Open University of Catalonia,
Tuesday, May 3, 2016, 15:30 - 18:00
C. Costa, C. Laoudias, A. Konstantinidis, G. Chatzimilioudis and D. Zeinalipour-Yazti
Data Management Systems Laboratory
Department of Computer Science
University of Cyprus
http://dmsl.cs.ucy.ac.cy/

## Slide 2: Motivation
People spend 80-90% of their time indoors – USA Environmental Protection Agency 2011.
>85% of data and 70% of voice traffic originates from within buildings – Nokia 2012.

## Slide 3: Localization Technologies
Modern trend in Localization are Internet-based Indoor Navigation (IIN) services founded on measurements collected by smart devices.
Technologies:
  Wi-Fi APs, Cellular Towers, other stationary antennas
  IMU Data (Gyroscope, Accelerometers, Digital Compass)
  Magnetic Field Sensors
  Beacons (BLE Beacons, RFID Active & Passive Beacons)
  Sound (Microphone), Light (Light Sensor), …

## Slide 4: Indoor Applications
Huge spectrum of indoor apps
  Navigation, Manufacturing, Asset Tracking, Inventory Management
  Healthcare, Smart Houses, Elderly support, Fitness apps
  Augmented Reality and many more.
Indoor Revenues expected reach 10B USD in 2020
  ABIresearch, “Retail Indoor Location Market Breaks US$10 Billion in 2020”’ Available at: https://goo.gl/ehPRMn, May 12, 2015.
Overview Publication / Tutorial:
  "Internet-based Indoor Navigation Services", IEEE Internet Computing (IC'16), http://goo.gl/VJjMRH
  Tutorial at IEEE MDM’15 (slides):
  http://goo.gl/70JV4q

## Slide 5: Anyplace IIN Service
http://anyplace.cs.ucy.ac.cy/
A complete open-source IIN Service developed at the University of Cyprus.
  Aims to become the predominant open-source Indoor Localization Service.
  Active community: Germany, Russia,
  Australia, Canada, UK, etc. – Join today!
  Android, Windows, iOS, JSON API

## Slide 6: Showcase I: Hotel in Pittsburgh, USA
Before 
(using Google API Location)
After 
(using Anyplace Location & Indoor Models)

## Slide 7: Showcase I: Hotel in Pittsburgh, USA
Modeling + Crowdsourcing

## Slide 8: Showcase: Univ. of Cyprus
Office Navigation @ Univ. of Cyprus
  Outdoor-to-Indoor Navigation through URL.
  60 Buildings mapped, Thousands of POIs (stairways, WC, elevators, equipment, etc.)
http://goo.gl/ns3lqN
Example:

## Slide 9: Other Showcases
Univ. of Würzburg, Institut für Informatik
  Mapped in about 1 hour
Universidad de Jaén, Spain
  Campus Navigation (9 Buildings)
Univ. of Mannheim, Library
  Aims to offer Navigation-to-Shelf

## Slide 10: Anyplace Open Maps
http://anyplace.cs.ucy.ac.cy/

## Slide 11: Presentation Outline
Introduction
Location Accuracy
  IEEE MDM’12, ACM IPSN’14, ACM IPSN’15, IEEE IC’16
Location Prefetching
  IEEE MDM’15
Future Challenges
  IEEE TKDE’15

## Slide 12: Location Accuracy
Rainer Mautz, ETH Zurich, 2011
: Spatial extension where system performance must be guaranteed
| Indoor |
| Outdoor |
Room Level Accuracy

## Slide 13: Location Accuracy
Source: NASA
Infrastructure-free systems: don’t require dedicated equipment for the provisioning of location signals (e.g., GPS, Wi-Fi, Cellular, Magnetic, IMU)
Infrastructure-based systems: require dedicated equipment (e.g., proprietary transmitters, beacons, antennas and cabling)
  Bluetooth Low Energy (BLE) beacons: iBeacons (Apple)
  Ultrasound: ALPS (CMU)
  Visible Light: EPSILON (Microsoft Research)
  Ultra Wide Band (UWB): Decawave
Anyplace Focus

## Slide 14
References
  [Airplace] "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias et. al., Best Demo Award at IEEE MDM'12. (Open Source!)
  [HybridCywee] "Indoor Geolocation on Multi-Sensor Smartphones", C.-L. Li, C. Laoudias, G. Larkou, Y.-K. Tsai, D. Zeinalipour-Yazti and C. G. Panayiotou, in ACM Mobisys'13. Video at: http://youtu.be/DyvQLSuI00I
  [UcyCywee] IPSN’14 Indoor Localization Competition (Microsoft Research), Berlin, Germany, April 13-14, 2014. 2nd Position with 1.96m! http://youtu.be/gQBSRw6qGn4
    D. Lymberopoulos, J. Liu, X. Yang, R. R. Choudhury, ..., C. Laoudias, D. Zeinalipour-Yazti, Y.-K. Tsai, and et. al., “A realistic evaluation and comparison of indoor location technologies: Experiences and lessons learned”, In IEEE/ACM IPSN 2015.
  1st Position at EVARILOS Open Challenge, European Union (TU Berlin, Germany), 2014.
Cywee / Airplace
WiFi Fingerprinting in Anyplace

## Slide 15: WiFi Fingerprinting
Received Signal Strength indicator (RSSI)
  Power measurement present in a received radio signal measured in dBm (Decibel-milliwatts)
    Max RSSI (-30dBm) to Min RSSI: (−90 dBm)
Advantages
  Readily provided by smartphone APIs
  Low power 125mW (RSSI) vs. 400 mW (transmit)
Disadvantages
  Complex propagation conditions (multipath, shadowing) due to wall, ceilings.
  RSS fluctuates over time at a given location (especially in open spaces).
  Unpredictable factors (people moving, doors, humidity)
’00

## Slide 16: Logging in Anyplace
Video
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015

## Slide 17: Hybrid Wi-Fi/IMU/Outdoor Anyplace
Video
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015

## Slide 18: Presentation Outline
Introduction
Location Accuracy
  IEEE MDM’12, ACM IPSN’14, ACM IPSN’15, IEEE IC’16
Location Prefetching
  IEEE MDM’15
Future Challenges
  IEEE TKDE’15

## Slide 19: Intermittent Connectivity
Problem: Wi-Fi coverage might be irregularly available inside buildings due to poor WLAN planning or due to budget constraints.
A user walking inside a Mall in Cyprus
  Whenever the user enters a store the RSSI indicator falls below a connectivity threshold -85dBm. (-30dbM to -90dbM)
  When disconnected IIN can’t offer navigation anymore 

## Slide 20: Intermittent Connectivity
IIN Service
Where-am-I?
 Intermittent Connectivity
Where-am-I?
Where-am-I?
No Navigation
Time
X

## Slide 21: PreLoc Navigation
IIN Service
Prefetch K RM rows
 Intermittent Connectivity
Prefetch K RM rows
Time
Prefetch K RM rows
X
Localize from Cache

## Slide 22: PreLoc Partitioning Step
Why? RM might contain many points (45K in CSUCY!).
Action: The objective of this step is to cluster these into groups so that they are easier to prefetch.
K-Means simple well-established clustering algorithm.
  Operation: Random Centroids (C), Add to Closest C, Re-adjust C
  Re-adjusting Centroids expensive quadratic complexity 

## Slide 23: PreLoc Partitioning Step
We use the Bradley-Fayyad-Reina (BFR)* algorithm
  A variant of k-means designated for large datasets.
  Instead of computing L2 distance of point p against centroid, as in k-means, it computes the Mahalanobis distance (distMah) against some set statistics (μ, σ).
  In BFR if distMah is less than a threshold add to set, else retain to possibly shape new clusters.
  Advantage: Less centroid computations! Points are traversed only once which is fast for big data!
μ
σ
Point (p)
distMah
Scaling Clustering Algorithms to Large Databases.. PS Bradley, UM Fayyad, C Reina - KDD, 1998

## Slide 24: PreLoc Selection Step
The Selection Step aims to sequence the retrieval of clusters, such that the most important clusters are downloaded first.
Question: Which clusters should a user download at a certain position if Wi-Fi not available next?
  PreLoc prioritizes the download of RM entries using historic traces of user inside the building !!!
User Current Location

## Slide 25: Presentation Outline
Introduction
Location Accuracy
  IEEE MDM’12, ACM IPSN’14, ACM IPSN’15, IEEE IC’16
Location Prefetching
  IEEE MDM’15
Future Challenges
  IEEE TKDE’15

## Slide 26
Massively process RSS log traces to generate a valuable Radiomap
Processing current logs in Anyplace for a single building takes several minutes!
Challenges in MapReduce:
  Collect Statistics (count, RSSI mean and standard deviation)
  Remove Outlier Values.
  Handle Diversity Issues
Big-Data Challenges

## Slide 27
Quality: Unreliable Crowdsourcers, Multi-device Issues, Hardware Outliers, Temporal Decay, etc.
  Remark: There is a Linear Relation between RSS values of devices.
  Challenge: Can we exploit this to align reported RSS values?
"Crowdsourced Indoor Localization for Diverse Devices through Radiomap Fusion", C. Laoudias, D. Zeinalipour-Yazti and C. G. Panayiotou, "Proceedings of the 4th Intl. Conference on Indoor Positioning and Indoor Navigation" (IPIN '13), Montbeliard-Belfort France, 2013.
Crowdsourcing Challenges

## Slide 28: Modeling Challenges
Indoor spaces exhibit complex topologies. They are composed of entities that are unique to indoor settings:
  e.g., rooms and hallways that are connected by doors.
  Conventional Euclidean distances are inapplicable in indoor space, e.g., NN of p1 is p2 not p3.
Jensen et. al. 2010
IndoorGML by OGC

## Slide 29: Location Privacy Challenges
An IIN Service can continuously “know” (surveil, track or monitor) the location of a user while serving them.
Location tracking is unethical and can even be illegal if it is carried out without the explicit user consent.
Imminent privacy threat, with greater impact that other privacy concerns, as it can occur at a very fine granularity. It reveals:
  The stores / products of interest in a mall.
  The book shelves of interest in a library
  Artifacts observed in a museum, etc.

## Slide 30: Location Privacy
IIN Service
...
I can see these Reference Points, where am I?
(x,y)!
User u
Towards planet-scale localization on smartphones with a partial radiomap", A. Konstantinidis, G. Chatzimilioudis, C. Laoudias, S. Nicolaou and D. Zeinalipour-Yazti. In ACM HotPlanet'12, in conjunction with ACM MobiSys '12, ACM, Pages: 9--14, 2012.
Privacy-Preserving Indoor Localization on Smartphones, Andreas Konstantinidis, Paschalis Mpeis, Demetrios Zeinalipour-Yazti and Yannis Theodoridis, in IEEE TKDE’15.

## Slide 31: Temporal Vector Map (TVM)
IIN Service
WiFi
WiFi
WiFi
...
Bloom Filter (u's APs)
K=3 Positions
User u
Set Membership Queries

## Slide 32: TVM Continuous
Camouflage trajectories
IIN determnines u’s location by exclusion

## Slide 33: Anyplace Indoor Information Service
Department of Computer Science, Open University of Catalonia,
Tuesday, May 3, 2016, 15:30 - 18:00
C. Costa, C. Laoudias, A. Konstantinidis, G. Chatzimilioudis and D. Zeinalipour-Yazti
Thanks – Questions?
http://dmsl.cs.ucy.ac.cy/

## Slide 34: WiFi Positioning Demo
  "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias, G. Constantinou, M. Constantinides, S. Nicolaou, D. Zeinalipour-Yazti, C. G. Panayiotou, Best Demo Award at IEEE MDM'12. (Open Source!)
Video
Works best in confined areas