## Slide 1: Internet-based Indoor Navigation Services
ACROSS Meeting, Centrum Wiskunde & Informatica (CWI),
Amsterdam, Netherlands, February 25, 2016.
Demetris Zeinalipour
Assistant Professor
Data Management Systems Laboratory
Department of Computer Science
University of Cyprus
http://www.cs.ucy.ac.cy/~dzeina/

## Slide 2: Motivation
People spend 80-90% of their time indoors – USA Environmental Protection Agency 2011.
>85% of data and 70% of voice traffic originates from within buildings – Nokia 2012.

## Slide 3: Localization Technologies
Modern trend in Localization are Internet-based Indoor Navigation (IIN) services founded on measurements collected by smart devices.
Technologies:
  Wi-Fi APs, Cellular Towers, other stationary antennas
  IMU Data (Gyroscope, Accelerometers, Digital Compass)
  Magnetic Field Sensors
  Beacons (BLE Beacons, RFID Active & Passive Beacons)
  Sound (Microphone), Light (Light Sensor), …

## Slide 4: Indoor Applications
Huge spectrum of indoor apps
  Navigation, Manufacturing, Asset Tracking, Inventory Manage
  Healthcare, Smart Houses, Elderly support, Fitness apps
  Augmented Reality and many more.
Indoor Revenues expected reach 10B USD in 2020
  ABIresearch, “Retail Indoor Location Market Breaks US$10 Billion in 2020”’ Available at: https://goo.gl/ehPRMn, May 12, 2015.
Overview Publication / Tutorial:
  "Internet-based Indoor Navigation Services", IEEE Internet Computing (IC'16), http://goo.gl/VJjMRH
  Tutorial at IEEE MDM’15 (slides):
  http://goo.gl/70JV4q

## Slide 5: Anyplace IIN Service
http://anyplace.cs.ucy.ac.cy/
An complete open-source IIN Service developed at the University of Cyprus.
Element for Indoor Accuracy in Internet of Services (IoS)!

## Slide 6: Anyplace Accuracy
http://anyplace.cs.ucy.ac.cy/
A) Accuracy (1.96 m )
  3 Intl. Awards (IPSN’14, MDM’12 and EVARILOS’14)
  2nd most accurate technology @ Microsoft Research Indoor Localization Competition, Berlin, Germany. – IPSN’15.
B) Open Source - https://github.com/dmsl/anyplace/
  Android, Windows, iOS, JSON API sources available on Github!
  Aims: Establish Anyplace as the predominant open-source Indoor Localization Service (as-a-Service or stand-alone)
  Active community with developers in Germany, Russia, Australia, Canada, UK, etc. – Join today!

## Slide 7: Anyplace Accuracy
Video

## Slide 8: Anyplace Crowdsourcing
http://anyplace.cs.ucy.ac.cy/
C) Crowdsourcing
Distributed Wi-Fi data collection through an open call.
Contributions through “Logger” and quality monitoring in “Architect”
Big data alignment of signals to remove noise using MapReduce.
"Crowdsourcing with smartphones", Georgios Chatzimiloudis, Andreas Konstantinidis, Christos Laoudias and Demetrios Zeinalipour-Yazti, IEEE Internet Computing (IC '12), Special Issue: Sep/Oct 2012 - Crowdsourcing, May 2012. IEEE Press, Vol. 16, Iss. 5, pp. 36-44, 2012.
  "Internet-based Indoor Navigation Services", IEEE Internet Computing (IC'16), http://goo.gl/VJjMRH

## Slide 9: Anyplace Features: Community
http://anyplace.cs.ucy.ac.cy/
D) Community
Already thousands of mapping attempts worldwide!

## Slide 10: Showcase: Univ. of Cyprus
Office Navigation @ Univ. of Cyprus
  Outdoor-to-Indoor Navigation through URL.
  60 Buildings mapped, Thousands of POIs (stairways, WC, elevators, equipment, etc.)
http://goo.gl/ns3lqN
Example:

## Slide 11: Other Showcases
Univ. of Wurzburg, Institute fur Informatik
  Mapped in about 1 hour
Universidad de Jaén, Spain
  Campus Navigation (9 Buildings)
Univ. of Mannheim, Library
  Aims to offer Navigation-to-Shelf

## Slide 12: Presentation Outline
Introduction & Anyplace
Research Challenges
  Location Privacy
    ACM HotPlanet’12, IEEE TKDE’15
  Radiomap Prefetching
    IEEE MDM’15
Future Challenges
  Big Data, Crowdsourcing, Modeling
    IEEE Internet Computing’16, IPIN’13.

## Slide 13: Location Privacy
IIN Service
...
I can see these Reference Points, where am I?
(x,y)!
User u
Towards planet-scale localization on smartphones with a partial radiomap", A. Konstantinidis, G. Chatzimilioudis, C. Laoudias, S. Nicolaou and D. Zeinalipour-Yazti. In ACM HotPlanet'12, in conjunction with ACM MobiSys '12, ACM, Pages: 9--14, 2012.
Privacy-Preserving Indoor Localization on Smartphones, Andreas Konstantinidis, Paschalis Mpeis, Demetrios Zeinalipour-Yazti and Yannis Theodoridis, in IEEE TKDE’15.

## Slide 14: Temporal Vector Map (TVM)
IIN Service
WiFi
WiFi
WiFi
...
Bloom Filter (u's APs)
K=3 Positions
User u
Set Membership Queries

## Slide 15: TVM – Bloom Filters
Bloom filters – basic idea:
  allocate a vector of b bits, initially all set to 0
  use h independent hash functions to hash every Access Point seen by a user to the vector.
The IIN Service selects any RadioMap row that has an AP belonging to the query bloom filter and send it to the user.
0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
AP2
AP13
AP2
AP13
b

## Slide 16: TVM – Bloom Filters
The most significant feature of Bloom filters is that there is a clear tradeoff between b and the probability of a false positive.
  Small b: Too many false positives (too much hiding & data download cost)
  Large b: “No” false positives (no hiding & no data download cost)
Given h optimal hash functions, b bits for the Bloom filter we can estimate the amount of false positives produced by the Bloom filter:
  False Positive Ratio:
  Size of vector:

## Slide 17: TVM Continuous
Camouflage trajectories
IIN determnines u’s location by exclusion

## Slide 18: TVM Evaluation
Energy required for 300 localization tasks (CPU+Wi-Fi) using PowerTutor on Android
  Campus (20MB)
  Town (100MB)
  City (1GB)
  Country (20GB)

## Slide 19: Presentation Outline
Introduction & Anyplace
Research Challenges
  Location Privacy
    ACM HotPlanet’12, IEEE TKDE’15
  Radiomap Prefetching
    IEEE MDM’15
Future Challenges
  Big Data, Crowdsourcing, Modeling
    IEEE Internet Computing’16, IPIN’13.

## Slide 20: Intermittent Connectivity
Problem: Wi-Fi coverage might be irregularly available inside buildings due to poor WLAN planning or due to budget constraints.
A user walking inside a Mall in Cyprus
  Whenever the user enters a store the RSSI indicator falls below a connectivity threshold -85dBm. (-30dbM to -90dbM)
  When disconnected IIN can’t offer navigation anymore 

## Slide 21: Intermittent Connectivity
IIN Service
Where-am-I?
 Intermittent Connectivity
Where-am-I?
Where-am-I?
No Navigation
Time
X

## Slide 22: PreLoc Navigation
IIN Service
Prefetch K RM rows
 Intermittent Connectivity
Prefetch K RM rows
Time
Prefetch K RM rows
X
Localize from Cache

## Slide 23: PreLoc Selection Step
The Selection Step aims to sequence the retrieval of clusters, such that the most important clusters are downloaded first.
Question: Which clusters should a user download at a certain position if Wi-Fi not available next?
  PreLoc prioritizes the download of RM entries using historic traces modelled as Directed Graphs.
User Current Location

## Slide 24: PreLoc Selection Step
PreLoc relies on the Probabilistic Group Selection (PGS) Heuristic to determine the RM entries to prefetch next.
A
B
C
D
A
1.0
D
B
C
0.33
1.0
0.66
0.5
Historic Traces
Dependency Graph
(DG)
(statistically independent transitions between vertices + no stationary transitions in historic traces)
Probabilistic k=3 Group Selection
Do Best First Search Traversal of DG from A:
follow the most promising option using priority queue.
P(A,B)=1.0
P(A,B,D)=0.66
P(A,B,D,C)=0.66*0.5=0.33
P(A,B,D,A) => cycle
P(A,B,D,C,D)=> cycle
P(A,B,C)=0.33
Empty queue – finished!
0.5
User Current Location
Early stop!

## Slide 25: Presentation Outline
Introduction & Anyplace
Research Challenges
  Location Privacy
    ACM HotPlanet’12, IEEE TKDE’15
  Radiomap Prefetching
    IEEE MDM’15
Future Challenges
  Big Data, Crowdsourcing, Modeling
    IEEE Internet Computing’16, IPIN’13.

## Slide 26
Massively process RSS log traces to generate a valuable Radiomap
Processing current logs in Anyplace for a single building takes several minutes!
Challenges in MapReduce:
  Collect Statistics (count, RSSI mean and standard deviation)
  Remove Outlier Values.
  Handle Diversity Issues
Big-Data Challenges

## Slide 27
Quality: Unreliable Crowdsourcers, Multi-device Issues, Hardware Outliers, Temporal Decay, etc.
  Remark: There is a Linear Relation between RSS values of devices.
  Challenge: Can we exploit this to align reported RSS values?
"Crowdsourced Indoor Localization for Diverse Devices through Radiomap Fusion", C. Laoudias, D. Zeinalipour-Yazti and C. G. Panayiotou, "Proceedings of the 4th Intl. Conference on Indoor Positioning and Indoor Navigation" (IPIN '13), Montbeliard-Belfort France, 2013.
Crowdsourcing Challenges

## Slide 28: Modeling Challenges
Indoor spaces exhibit complex topologies. They are composed of entities that are unique to indoor settings:
  e.g., rooms and hallways that are connected by doors.
  Conventional Euclidean distances are inapplicable in indoor space, e.g., NN of p1 is p2 not p3.
Jensen et. al. 2010
IndoorGML by OGC

## Slide 29: Internet-based Indoor Navigation Services
ACROSS Meeting, Centrum Wiskunde & Informatica (CWI),
Amsterdam, Netherlands, February 25, 2016.
Thanks! Questions?
Demetris Zeinalipour
Data Management Systems Laboratory
Department of Computer Science
University of Cyprus
http://www.cs.ucy.ac.cy/~dzeina/