## Slide 1: Indoor Data Management in Anyplace
University of Mannheim, Chair of Information Systems II, Mannheim, Germany, May 4, 2017
Demetris Zeinalipour
Assistant Professor
Department of Computer Science, University of Cyprus, Cyprus
Humboldt Fellow @ Max Planck Institute for Informatics, Germany
http://www.cs.ucy.ac.cy/~dzeina/
dzeina@cs.ucy.ac.cy

## Slide 2: Motivation
People spend 80-90% of their time indoors – USA Environmental Protection Agency 2011.
>85% of data and 70% of voice traffic originates from within buildings – Nokia 2012.

## Slide 3: Localization Technologies
Modern trend in Localization are Internet-based Indoor Navigation (IIN) services founded on measurements collected by smart devices.
Technologies:
  Wi-Fi APs, Cellular Towers, other stationary antennas
  IMU Data (Gyroscope, Accelerometers, Digital Compass)
  Magnetic Field Sensors
  Beacons (BLE Beacons, RFID Active & Passive Beacons)
  Sound (Microphone), Light (Light Sensor), …

## Slide 4: Indoor Applications
Huge spectrum of indoor apps
  Navigation, Manufacturing, Asset Tracking, Inventory Manag.
  Healthcare, Smart Houses, Elderly support, Fitness apps
  Augmented Reality and many more.
Indoor Revenues expected reach 10B USD in 2020
  ABIresearch, “Retail Indoor Location Market Breaks US$10 Billion in 2020”’ Available at: https://goo.gl/ehPRMn, May 12, 2015.
Tutorial @ IEEE MDM’15
  “Mobile Data Management in Indoor Spaces”, Christos Laoudias and Demetrios Zeinalipour-Yazti
  Slides available: http://goo.gl/70JV4q

## Slide 5: Anyplace IIN Service
http://anyplace.cs.ucy.ac.cy/
Anyplace: A complete IIN Service open for research and development
  Accuracy (1.96m [ACM IPSN’15])
  Crowdsourcing [IEEE IC’12]
  Privacy [IEEE TKDE’15],
  Other: Modeling [SIGSPATIAL’17-S]
Model Your Building!
  It takes 1 minute to get your model online – 1 hour to offer indoor navigation and search in a 2500 sq meter building!
  "Internet-based Indoor Navigation Services", Demetrios Zeinalipour-Yazti, Christos Laoudias, Kyriakos Georgiou and Georgios Chatzimiloudis, IEEE Internet Computing (IC'17), IEEE Computer Society, 2017.

## Slide 6: Anyplace @ MDM’15
Before 
(using Google API Location)
After 
(using Anyplace Location & Indoor Models)

## Slide 7: Anyplace @ MDM’15
Modeling + Crowdsourcing

## Slide 8: Showcase: Univ. of Cyprus
Office Navigation @ Univ. of Cyprus
  Outdoor-to-Indoor Navigation through URL.
  60 Buildings mapped, Thousands of POIs (stairways, WC, elevators, equipment, etc.)
http://goo.gl/ns3lqN
Example:

## Slide 9: Campus and Library Navigation
Univ. of Würzburg, Institut für Informatik
  Mapped in about 1 hour
Universidad de Jaén, Spain - Campus
  Campus Navigation (9 Buildings)
Univ. of Mannheim, Library
  Aim: book navigation in Westflügel

## Slide 10: Anyplace Open Maps
http://anyplace.cs.ucy.ac.cy/
~1,000 mapping attempts
~100,000 user interactions
~20,000 users visited
More than 80 forks on Github

## Slide 11: Presentation Outline
Introduction
Location Accuracy
  MDM’12, IPSN’14, IPSN’15
Location Privacy
  HotPlanet’12, IEEE TKDE’15
Radiomap Prefetching
  MDM’15
Future Challenges

## Slide 12: Location Accuracy
Rainer Mautz, ETH Zurich, 2011
: Spatial extension where system performance must be guaranteed
| Indoor |
| Outdoor |
Room Level Accuracy
Ultrasound:
AOA, TOA, TDOA, signal reflection
Infrared (IR)
Firefly delivers 3mm accuracy
Ultra Wide Band (UWB)
TOA, TDOA
Radio Frequency IDentification (RFID)
Cell of Origin, Signal Strength

## Slide 13: Location Accuracy
Source: NASA
Infrastructure-free systems: don’t require dedicated equipment for the provisioning of location signals (e.g., GPS, Wi-Fi, Cellular, Magnetic, IMU)
Infrastructure-based systems: require dedicated equipment (e.g., proprietary transmitters, beacons, antennas and cabling)
  Bluetooth Low Energy (BLE) beacons: iBeacons (Apple)
  Ultrasound: ALPS (CMU)
  Visible Light: EPSILON (Microsoft Research)
  Ultra Wide Band (UWB): Decawave
Anyplace Focus

## Slide 14: Location (Outdoor/Indoor)
Cell ID:
  Cell ID is the Unique Identifier of Cellular Towers.
Cell ID Databases
  Skyhook Wireless (2003), MA, USA (Apple, Samsung): 30 million+ cell towers, 1 Billion Wi-Fi APs, 1 billion+ geolocated IPs, 7 billion+ monthly location requests and 2.5 million geofencable POIs.
  Google Geolocation “Big” Database (similar)
Disadvantages:
Low accuracy: 30-50m (indoor) to 1-30km (outdoor).
Serving cell is not always the nearest.

## Slide 15: Location (Indoor)
Inertial Measurement Units (IMU)
  3D acceleration, 3D gyroscope, digital compass using dead reckoning (calculate next position based on prior).
Disadvantages
  Suffers from drift (difference between where the system thinks it is located, and the actual location)
Advantages
  Sensors are available on smartphones.
  Newer smartphones (iphone 5s) have motion co-processors always-on reading sensors and even providing activitity classifiers (driving, walking, running, etc.)

## Slide 16
References
  [Airplace] "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias et. al., Best Demo Award at IEEE MDM'12. (Open Source!)
  [HybridCywee] "Indoor Geolocation on Multi-Sensor Smartphones", C.-L. Li, C. Laoudias, G. Larkou, Y.-K. Tsai, D. Zeinalipour-Yazti and C. G. Panayiotou, in ACM Mobisys'13. Video at: http://youtu.be/DyvQLSuI00I
  [UcyCywee] IPSN’14 Indoor Localization Competition (Microsoft Research), Berlin, Germany, April 13-14, 2014. 2nd Position with 1.96m! http://youtu.be/gQBSRw6qGn4
    D. Lymberopoulos, J. Liu, X. Yang, R. R. Choudhury, ..., C. Laoudias, D. Zeinalipour-Yazti, Y.-K. Tsai, and et. al., “A realistic evaluation and comparison of indoor location technologies: Experiences and lessons learned”, In IEEE/ACM IPSN 2015.
  1st Position at EVARILOS Open Challenge, European Union (TU Berlin, Germany), 2014.
Cywee / Airplace
WiFi Fingerprinting in Anyplace

## Slide 17: WiFi Fingerprinting
Received Signal Strength indicator (RSSI)
  Power measurement present in a received radio signal measured in dBm (Decibel-milliwatts)
    Max RSSI (-30dBm) to Min RSSI: (−90 dBm)
Advantages
  Readily provided by smartphone APIs
  Low power 125mW (RSSI) vs. 400 mW (transmit)
Disadvantages
  Complex propagation conditions (multipath, shadowing) due to wall, ceilings.
  RSS fluctuates over time at a given location (especially in open spaces).
  Unpredictable factors (people moving, doors, humidity)
’00

## Slide 18: WiFi Fingerprinting
Mapping Area with WiFi Fingerprints
  n APs deployed in the area
  Fingerprints ri = [ ri1, ri2, …, rin]
  Averaging

## Slide 19: WiFi Fingerprinting
Mapping Area with WiFi Fingerprints
  Repeat process for rest points in building. (IEEE MDM’12)
  Use 4 direction mapping (NSWE) to overcome body blocking or reflecting the wireless signals.
  Collect measurements while walking in straight lines (IPIN’14)

## Slide 20: Logging in Anyplace
Video
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015

## Slide 21: WiFi Positioning
Positioning with WiFi Fingerprint
  Collect Fingerprint s = [ s1, s2, …, sn]
  Compute distance || ri - s || and position user at:
    Nearest Neighbor (NN)
    K Nearest Neighbors (wi = 1 / K) [convex combination of k loc]
    Weighted K Nearest Neighbors (wi = 1 / || ri - s || )
s = [ -70, -51]
RadioMap
r1 = [ -71, -82, (x1,y1)]
r2 = [ -65, -80, (x2,y2)]
…
rN = [ -73, -44, (xN,yN)]
NN, KNN, WKNN

## Slide 22: WiFi Positioning Demo
  "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias, G. Constantinou, M. Constantinides, S. Nicolaou, D. Zeinalipour-Yazti, C. G. Panayiotou, Best Demo Award at IEEE MDM'12. (Open Source!)
Video
Works best in confined areas

## Slide 23: Hybrid Wi-Fi/IMU/Outdoor Anyplace
Video
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015

## Slide 24: Presentation Outline
Introduction
Location Accuracy
  MDM’12, IPSN’14, IPSN’15
Location Privacy
  HotPlanet’12, IEEE TKDE’15
Radiomap Prefetching
  MDM’15
Future Challenges

## Slide 25: Location Privacy
An IIN Service can continuously “know” (surveil, track or monitor) the location of a user while serving them.
Location tracking of known individuals is unethical and can even be illegal if it is carried out without the explicit user consent.
Imminent privacy threat, with greater impact that other privacy concerns, as it can occur at a very fine granularity. It reveals:
  The stores / products of interest in a mall.
  The book shelves of interest in a library
  Artifacts observed in a museum, etc.

## Slide 26: Location Privacy
IIN services might become attractive targets for hackers, aiming to steal location data and carry out illegal acts (e.g., break into houses).
IIN should be considered as fundamentally untrusted entities, so we aim to devise techniques that allow the exploitation of IIN utility with controllable privacy to the user.
Privacy vs. No Privacy
  Location Privacy: when location estimated by user device (current Anyplace) – data is outdated 
  No Location Privacy: when the location is derived continuously by the IIN (most IIN services)

## Slide 27: Location Privacy
IIN Service
...
I can see these Reference Points, where am I?
(x,y)!
User u
Towards planet-scale localization on smartphones with a partial radiomap", A. Konstantinidis, G. Chatzimilioudis, C. Laoudias, S. Nicolaou and D. Zeinalipour-Yazti. In ACM HotPlanet'12, in conjunction with ACM MobiSys '12, ACM, Pages: 9--14, 2012.
Privacy-Preserving Indoor Localization on Smartphones, Andreas Konstantinidis, Paschalis Mpeis, Demetrios Zeinalipour-Yazti and Yannis Theodoridis, in IEEE TKDE’15.

## Slide 28: Temporal Vector Map (TVM)
IIN Service
WiFi
WiFi
WiFi
...
Bloom Filter (u's APs)
K=3 Positions
User u
Set Membership Queries

## Slide 29: TVM – Bloom Filters
Bloom filters – basic idea:
  allocate a vector of b bits, initially all set to 0
  use h independent hash functions to hash every Access Point seen by a user to the vector.
The IIN Service selects any RadioMap row that has an AP belonging to the query bloom filter and send it to the user.
0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
AP2
AP13
AP2
AP13
b

## Slide 30: TVM – Bloom Filters
The most significant feature of Bloom filters is that there is a clear tradeoff between b and the probability of a false positive.
  Small b: Too many false positives (too much hiding & cost)
  Large b: “No” false positives (no hiding & no cost)
Given h optimal hash functions, b bits for the Bloom filter we can estimate the amount of false positives produced by the Bloom filter:
  False Positive Ratio:
  Size of vector:

## Slide 31: TVM Evaluation
Energy required for 300 localization tasks (CPU+Wi-Fi) using PowerTutor on Android
  Campus (20MB)
  Town (100MB)
  City (1GB)
  Country (20GB)

## Slide 32: TVM Continuous
Camouflage trajectories
IIN determnines u’s location by exclusion

## Slide 33: Presentation Outline
Introduction
Location Accuracy
  MDM’12, IPSN’14, IPSN’15
Location Privacy
  HotPlanet’12, IEEE TKDE’15
Radiomap Prefetching
  MDM’15
Future Challenges

## Slide 34: Intermittent Connectivity
Problem: Wi-Fi coverage might be irregularly available inside buildings due to poor WLAN planning or due to budget constraints.
A user walking inside a Mall in Cyprus
  Whenever the user enters a store the RSSI indicator falls below a connectivity threshold -85dBm. (-30dbM to -90dbM)
  When disconnected IIN can’t offer navigation anymore 

## Slide 35: Intermittent Connectivity
IIN Service
Where-am-I?
 Intermittent Connectivity
Where-am-I?
Where-am-I?
No Navigation
Time
X

## Slide 36: PreLoc Navigation
IIN Service
Prefetch K RM rows
 Intermittent Connectivity
Prefetch K RM rows
Time
Prefetch K RM rows
X
Localize from Cache

## Slide 37: Intermittent Connectivity
Why not fallback from Wi-Fi to Mobile Internet (2G-4G) when Wi-Fi is not available?
Mobile Internet Limitations:
  Coverage: blockage or attenuation of signals in indoor spaces.
  Slow fallback between outdated Mobile Internet and Wi-Fi infrastructures.
    Lack of ubiquitous 802.11k, 802.11r (fast roaming) and 4G infrastructure.
  Limited Quota: Nobody ones to waste a mobile Internet plan for navigation purposes.
  Unavailability due to Roaming: when traveling and needing indoor navigation at most.

## Slide 38: PreLoc Partitioning Step
Why? RM might contain many points (45K in CSUCY!).
Action: The objective of this step is to cluster these into groups so that they are easier to prefetch.
K-Means simple well-established clustering algorithm.
  Operation: Random Centroids (C), Add to Closest C, Re-adjust C
  Re-adjusting Centroids expensive quadratic complexity 

## Slide 39: PreLoc Partitioning Step
We use the Bradley-Fayyad-Reina (BFR)* algorithm
  A variant of k-means designated for large datasets.
  Instead of computing L2 distance of point p against centroid, as in k-means, it computes the Mahalanobis distance (distMah) against some set statistics (μ, σ).
  In BFR if distMah is less than a threshold add to set, else retain to possibly shape new clusters.
  Advantage: Less centroid computations! Points are traversed only once which is fast for big data!
μ
σ
Point (p)
distMah
Scaling Clustering Algorithms to Large Databases.. PS Bradley, UM Fayyad, C Reina - KDD, 1998

## Slide 40: PreLoc Selection Step
The Selection Step aims to sequence the retrieval of clusters, such that the most important clusters are downloaded first.
Question: Which clusters should a user download at a certain position if Wi-Fi not available next?
  PreLoc prioritizes the download of RM entries using historic traces of users inside the building !!!
User Current Location

## Slide 41: PreLoc Selection Step
PreLoc relies on the Probabilistic Group Selection (PGS) Heuristic to determine the RM entries to prefetch next.
A
B
C
D
A
1.0
D
B
C
0.33
1.0
0.66
0.5
Historic Traces
Dependency Graph
(DG)
(statistically independent transitions between vertices + no stationary transitions in historic traces)
Probabilistic k=3 Group Selection
Do Best First Search Traversal of DG from A:
follow the most promising option using priority queue.
P(A,B)=1.0
P(A,B,D)=0.66
P(A,B,D,C)=0.66*0.5=0.33
P(A,B,D,A) => cycle
P(A,B,D,C,D)=> cycle
P(A,B,C)=0.33
Empty queue – finished!
0.5
User Current Location
Early stop!
Notes: Historic Traces example: four state random process

## Slide 42: Presentation Outline
Introduction
Location Accuracy
  MDM’12, IPSN’14, IPSN’15.
Location Privacy
  HotPlanet’12, IEEE TKDE’15
Radiomap Prefetching
  MDM’15
Future Challenges

## Slide 43: Big-Data Challenges
Massively process RSS log traces to generate a valuable Radiomap
Processing current logs in Anyplace for a single building takes several minutes!
Challenges in MapReduce:
  Collect Statistics (count, RSSI mean and standard deviation)
  Remove Outlier Values.
  Handle Diversity Issues

## Slide 44: Crowdsourcing Challenges
Quality: Unreliable Crowdsourcers, Multi-device Issues, Hardware Outliers, Temporal Decay, etc.
  Remark: There is a Linear Relation between RSS values of devices.
  Challenge: Can we exploit this to align reported RSS values?
"Crowdsourced Indoor Localization for Diverse Devices through Radiomap Fusion", C. Laoudias, D. Zeinalipour-Yazti and C. G. Panayiotou, "Proceedings of the 4th Intl. Conference on Indoor Positioning and Indoor Navigation" (IPIN '13), Montbeliard-Belfort France, 2013.

## Slide 45: Crowdsourcing Challenges
Problem: There is a mismatch between density of fingerprints and accuracy of the RadioMap (RM).
Solution: We use generic interpolation and a tool from estimation statistics to identify an accuracy estimator (lower bound)
"Indoor Localization Accuracy Estimation from Fingerprint Data", Artyom Nikitin, Georgios Chatzimilioudis, Christos Laoudias, Panagiotis Karras and Demetrios Zeinalipour-Yazti,
In IEEE MDM’17, Daejeon, South Korea, 2017
RM Density
RM Accuracy

## Slide 46: Modeling Challenges
Indoor spaces exhibit complex topologies. They are composed of entities that are unique to indoor settings:
  e.g., rooms and hallways that are connected by doors.
  Conventional Euclidean distances are inapplicable in indoor space, e.g., NN of p1 is p2 not p3.
Christian Becker, Frank Dürr, Personal and Ubiquitous Computing, 2005 => Jensen (2010)
IndoorGML by OGC

## Slide 47: Indoor Data Management in Anyplace
University of Mannheim, Chair of Information Systems II, Mannheim, Germany, May 4, 2017
Thanks! Questions?
Demetris Zeinalipour
Department of Computer Science, University of Cyprus, Cyprus
Humboldt Fellow @ Max Planck Institute for Informatics, Germany
http://www.cs.ucy.ac.cy/~dzeina/
dzeina@cs.ucy.ac.cy