## Slide 1: Mobile Data Management in Indoor Spaces
Christos Laoudias§ and Demetrios Zeinalipour-Yazti∗
§KIOS Research Center, University of Cyprus, 1678 Nicosia, Cyprus
∗Dept. of Computer Science, University of Cyprus, 1678 Nicosia, Cyprus
Advanced Seminar at 16th IEEE Int. Conference on Mobile Data Management (MDM’15), Pittsburgh, PA, USA, June 17, 2015
http://goo.gl/70JV4q

## Slide 2: Disclaimer
Feel free to use any of the following slides for educational purposes, however kindly acknowledge the source.
We would also like to know how you have used these slides, so please send us an email with comments or suggestions.
This presentation is available at:
http://dmsl.cs.ucy.ac.cy/tutorials/mdm15/

## Slide 3: About this Tutorial
The goal is to provide an overview of the emerging field of Indoor Data Management with a particular emphasis on Mobile Systems.
We tackle the topic from a wide range of perspectives:
  Fundamentals, Definitions, Current State
  Academic / Industrial Perspective
  Reality / Visionary Scenarios, Future Challenges…
Lots of examples and illustrations to keep this presentation entertaining and educating.
The seminar captures the big picture, such that interested researchers/practitioners can expand their study by following the references.

## Slide 4: Motivation
People spend 80-90% of their time indoors – USA Environmental Protection Agency 2011.
>85% of data and 70% of voice traffic originates from within buildings – Nokia 2012.

## Slide 5: Indoor Data Management
Indoor Data Management deals with all aspects of handling indoor data as a valuable resource:
  Localization (tracking) from data
  Modeling (symbolic vs. geometric)
  Indexing
  Query Processing & Privacy
  Energy-aware processing
In this talk, we will attempt to cover the current state but also identify future challenges.
Christian S. Jensen, Hua Lu, Bin Yang: Indoor - A New Data Management Frontier. IEEE Data Eng. Bull. 33(2): 12-17 (2010)

## Slide 6: Internet-based Indoor Navigation
Enablers for Indoor have been Internet-based Indoor Navigation (IIN)* services founded on measurements collected by smart devices.
“Internet-based Indoor Navigation Services” Zeinalipour-Yazti, Laoudias, Georgiou and Chatzimilioudis, in submission (magazine article upon which this tutorial is founded)
IIN Service
enrich
navigate

## Slide 7: IIN Applications
IIN is bringing a wide range of Applications:
  In-building Navigation: Museums, Airports, Malls
  Asset Tracking and Hospital Inventory Managem.
  Augmented Reality
  Smart Houses and Elderly support.
  More to be shown in subsequent slides.

## Slide 8: IIN Taxonomy
Explained Next

## Slide 9: Anyplace IIN Service
http://anyplace.cs.ucy.ac.cy/
Anyplace: A complete IIN Service open for research and development
  Accuracy (1.96m [IPSN’15])
  Crowdsourcing [IC’12]
  Privacy [TKDE’15], Openness [MDM’12]
  Other: Modeling, Modular, …
Model Your Building!
  It takes 1 minute to get your model online – 1 hour to offer indoor navigation and search in a 2500 sq meter building!
Don’t miss our MDM’15 Demos of Anyplace!
  Anyplace: A Crowdsourced Indoor Information Service , Kyriakos Georgiou Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti
  Tue. Jun 16, 15:30-17:00, Sterlings
  Thu. Jun 18, 13:30-15:00, Sterlings

## Slide 10: Anyplace IIN Workflow
IIN Service
a) Upload Measurements
b) Build RM (Radiomap)
c) Localize
Logger
Navigator
fingerprint

## Slide 11: Anyplace @ MDM’15
Before 
(using Google API Location)
After 
(using Anyplace Location & Indoor Models)

## Slide 12: Anyplace @ MDM’15
Model: 1 hour (Image & POIs)
Radiomap: 10 minutes / floor
  Could also use Google Indoor Maps (NOT frequently available and also NO fine location available! )

## Slide 13: Tutorial Outline
Introduction
Location
Modeling
Crowdsourcing
Privacy
Open Challenges

## Slide 14: Location
Location (position): identifies a point or an area on the Earth's surface.
  Localization = Positioning = Tracking: identifying location.
Indoor Location: identifies a point located inside a building.
  Developments for the last 15 years.
  Specialized conferences (e.g., IPIN) & competitions (IPSN)
  Expected Accuracy: cm - meters
Mobile-based Indoor Location: Indoor Location with the assistance of a mobile computing device (e.g., smartphone).
  Remainder of the tutorial focuses on this category!

## Slide 15: Location (Applications)
Rainer Mautz, ETH Zurich, 2011
: Spatial extension where system performance must be guaranteed
| Indoor |
| Outdoor |
Tutorial Scope
Ultrasound:
AOA, TOA, TDOA, signal reflection
Infrared (IR)
Firefly delivers 3mm accuracy
Ultra Wide Band (UWB)
TOA, TDOA
Radio Frequency IDentification (RFID)
Cell of Origin, Signal Strength

## Slide 16: Location (Technologies)
Rainer Mautz, ETH Zurich, 2011
: Spatial extension where system performance must be guaranteed
| Indoor |
| Outdoor |
Tutorial Scope
Ultrasound:
AOA, TOA, TDOA, signal reflection
Infrared (IR)
Firefly delivers 3mm accuracy
Ultra Wide Band (UWB)
TOA, TDOA
Radio Frequency IDentification (RFID)
Cell of Origin, Signal Strength

## Slide 17: Localization
Source: NASA
Infrastructure-free systems: don’t require dedicated equipment for the provisioning of location signals (e.g., GPS, Wi-Fi, Cellular, Magnetic, IMU)
Infrastructure-based systems: require dedicated equipment (e.g., proprietary transmitters, beacons, antennas and cabling)
  Bluetooth Low Energy (BLE) beacons: iBeacons (Apple)
  Ultrasound: ALPS (CMU)
  Visible Light: EPSILON (Microsoft Research)
  Ultra Wide Band (UWB): Decawave
Focus of next slides

## Slide 18: Location
Global Navigation Satellite Systems (GNSS) have played an important role in Outdoor (Spatial) Data Management:
  Current: Global Positioning System (US), GLONASS (Russian)
  Upcoming: Galileo (European), Indian Regional Navigation Satellite System (IRNASS), BeiDou-2 (Chinese)
Many civilian uses with advent of GIS technologies since ‘70 (ESRI)
Location-based Services
Precision Agriculture
Geographic Mapping
Navigation
Infrastructure-free

## Slide 19: Location (Outdoor)
GNSS Drawbacks for Indoor Location:
  Low availability indoors due to the blockage or attenuation of the satellite signals.
  High start-up time.
  Power Demanding (continuously receive signals).
Infrastructure-free

## Slide 20: Location (Outdoor/Indoor)
Cell ID:
  Cell ID is the Unique Identifier of Cellular Towers.
Cell ID Databases
  Skyhook Wireless (2003), MA, USA (Apple, Samsung): 30 million+ cell towers, 1 Billion Wi-Fi APs, 1 billion+ geolocated IPs, 7 billion+ monthly location requests and 2.5 million geofencable POIs.
  Google Geolocation “Big” Database (similar)
Disadvantages:
Low accuracy: 30-50m (indoor) to 1-30km (outdoor).
Serving cell is not always the nearest.
Infrastructure-free

## Slide 21: Public Cell ID Databases
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Wigle.net API
  2.8+ billion raw observations, 191+ million WiFi APs, 4.5+ M cell towers, 170.000 “stumblers” (wardrivers), leaderboards, access to raw data
Open Cell ID API
  7 million cell towers, access to raw data
Mozilla Location Service API
  8.5 million cell towers, 210+ million WiFi APs, 856+ million cell and 3.4+ billion WiFi observations, leader board, no access to raw data
Infrastructure-free

## Slide 22: Location (Indoor)
Inertial Measurement Units (IMU)
  3D acceleration, 3D gyroscope, digital compass using dead reckoning (calculate next position based on prior).
Disadvantages
  Suffers from drift (difference between where the system thinks it is located, and the actual location)
Advantages
  Sensors are available on smartphones.
  Newer smartphones (iphone 5s) have motion co-processors always-on reading sensors and even providing activitity classifiers (driving, walking, running, or sleeping, etc.)
Infrastructure-free

## Slide 23
References
  [Airplace] "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias et. al., Best Demo Award at IEEE MDM'12. (Open Source!)
  [HybridCywee] "Indoor Geolocation on Multi-Sensor Smartphones", C.-L. Li, C. Laoudias, G. Larkou, Y.-K. Tsai, D. Zeinalipour-Yazti and C. G. Panayiotou, in ACM Mobisys'13. Video at: http://youtu.be/DyvQLSuI00I
  [UcyCywee] IPSN’14 Indoor Localization Competition (Microsoft Research), Berlin, Germany, April 13-14, 2014. 2nd Position with 1.96m! http://youtu.be/gQBSRw6qGn4
    D. Lymberopoulos, J. Liu, X. Yang, R. R. Choudhury, ..., C. Laoudias, D. Zeinalipour-Yazti, Y.-K. Tsai, and et. al., “A realistic evaluation and comparison of indoor location technologies: Experiences and lessons learned”, In IEEE/ACM IPSN 2015.
  1st Position at EVARILOS Open Challenge, European Union (TU Berlin, Germany).
Cywee / Airplace
WiFi Fingerprinting in Anyplace
Infrastructure-free

## Slide 24: WiFi Fingerprinting
Received Signal Strength Indicator (RSSI)
  Power measurement present in a received radio signal measured in [ dBm, Decibel-milliwatts ]
    80 dBm = 100 kW Transmission power of FM radio (50 km)
    0 dBm = 1 mW
    -80dBm = 10 pW | Max RSSI (-30dBm) to Min RSSI: (−90 dBm)
    -110dBm = 0.01 pW | WiFi AP is visible but out of data range.
Advantages
  Readily provided by smartphone APIs .
  Low power 125mW (RSSI) vs. 400 mW (transmit)
Disadvantages
  Complex propagation conditions (multipath, shadowing) due to wall, ceilings.
  RSS fluctuates over time at a given location (especially in open spaces).
  Unpredictable factors (people moving, doors, humidity)
Infrastructure-free

## Slide 25: WiFi Fingerprinting
Mapping Area with WiFi Fingerprints
  n APs deployed in the area
  Fingerprints ri = [ ri1, ri2, …, rin]
  Averaging
Infrastructure-free

## Slide 26: WiFi Fingerprinting
Mapping Area with WiFi Fingerprints
  Repeat process for rest points in building. (IEEE MDM’12)
  Use 4 direction mapping (NSWE) to overcome body blocking or reflecting the wireless signals.
  Collect measurements while walking in straight lines (IPIN’14)
Infrastructure-free

## Slide 27: Logging in Anyplace
Video
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015
Infrastructure-free

## Slide 28: WiFi Positioning
Positioning with WiFi Fingerprint
  Collect Fingerprint s = [ s1, s2, …, sn]
  Compute distance || ri - s || and position user at:
    Nearest Neighbor (NN)
    K Nearest Neighbors (wi = 1 / K)
    Weighted K Nearest Neighbors (wi = 1 / || ri - s || )
s = [ -70, -51]
RadioMap
r1 = [ -71, -82, (x1,y1)]
r2 = [ -65, -80, (x2,y2)]
…
rN = [ -73, -44, (xN,yN)]
NN, KNN, WKNN
Infrastructure-free

## Slide 29: WiFi Positioning Demo
  "The Airplace Indoor Positioning Platform for Android Smartphones", C. Laoudias, G. Constantinou, M. Constantinides, S. Nicolaou, D. Zeinalipour-Yazti, C. G. Panayiotou, Best Demo Award at IEEE MDM'12. (Open Source!)
Video
Infrastructure-free

## Slide 30: Hybrid IMU/WiFi Positioning
We engaged in an Industrial NRE contract with Cywee Taiwan Ltd, a hardware/software motion processing company (ACM Mobisys’13)
The result was a Hybrid IMU/WiFi Positioning system with the following additional features:
  Location Fusion: WiFi / IMU (3-axis accelerometer, gyroscope, and digital compass) using a particle filter.
  MapMatching: to handle inaccurate IMU location estimates (e.g., void passing through walls).
  Magnetic Mapping: detect and handle magnetic abnormalities due to electrical appliances and refining the orientation.
Infrastructure-free

## Slide 31: Hybrid WiFi/IMU Positioning Demo
  “Indoor Geolocation on Multi-Sensor Smartphones", C.-L. Li, C. Laoudias, G. Larkou, Y.-K. Tsai, D. Zeinalipour-Yazti and C. G. Panayiotou, in ACM Mobisys'13.
  Video at: http://youtu.be/DyvQLSuI00I
Infrastructure-free

## Slide 32: Hybrid Wi-Fi/IMU/Outdoor Anyplace
Video
Infrastructure-free
"Anyplace: A Crowdsourced Indoor Information Service", Kyriakos Georgiou, Timotheos Constambeys, Christos Laoudias, Lambros Petrou, Georgios Chatzimilioudis and Demetrios Zeinalipour-Yazti, Proceedings of the 16th IEEE International Conference on Mobile Data Management (MDM '15), IEEE Press, Volume 2, Pages: 291-294, 2015

## Slide 33: Magnetic-based
Earth’s magnetic field
  Exploit indoor disturbances: power cables, elevators, metal surfaces, electrical appliances.
  Alternative for iOS and Windows phones where WiFi RSS is not available for fingerprinting (IndoorAtlas)
Source: wired.co.uk
Source: Wikipedia
Infrastructure-free

## Slide 34: Localization Outline
Source: NASA
Infrastructure-free systems: don’t require dedicated equipment for the provision of location signals on a modern smartphone (e.g., GPS, Wi-Fi, Cellular, Magnetic, IMU)
Infrastructure-based systems: require dedicated equipment (e.g., proprietary transmitters, beacons, antennas and cabling)
  Bluetooth Low Energy (BLE) beacons: iBeacons
  Ultrasound: ALPS (CMU)
  Visible Light: EPSILON (Microsoft Research)
  Ultra Wide Band (UWB): Decawave
Focus of next slides

## Slide 35: RFID Tags
Passive RFID
  Tag collects energy from transmitter to respond with a Unique ID.
  Range: 10cm to few meters
  Indicative Price: 0.25 cents / tag
Active RFID
  Tag is battery-powered (larger size), thus can transmit UID autonomously.
  Range: Hundreds of meters.
  Indicative Price: 10-50 USD / tag
Infrastructure-based
Older Trend

## Slide 36: Beacons
Source: NASA
iBeacon: Bluetooth Low Energy protocol by Apple (2013).
Beacon is a tiny battery powered devices that emits BLE signals.
  Transmits unique (changeable) identifiers that can be picked up by any Linux Bluetooth stack (iPhone-Android-Windows).
  e.g., UUID f7826da6-4fa2-4e98-8024-bc5b71e0893e (beacon set), Major 1 and 65535 (e.g., floor), Minor 1 and 65535 (e.g., room)
  Can also pick up periodical broadcasting packets (Probe Requests) made by smartphones to actively seek Wi-Fi Access Points (tracking usages).
Infrastructure-based

## Slide 37: Beacons
Source: NASA
Beacon Facts
  $5-$50 USD, Frequencies: 1Hz to 10Hz (1s to 100ms)
  Cell, AAA batteries (4-6 months) or USB powered
  Transmission Range: 1m to 50 m (-30dbm – 0dbm)
  Might contain sensors: temperature, motion (estimote)
  (e.g., open fitness app when bicycle starts moving)
Which beacon to use?
  AisleLabs, May 4, 2015.
  http://goo.gl/ej9P0n
Indoo.rs SF Airport deploy:
  300 StickNFind (15K USD)
  60,000 m2
Infrastructure-based

## Slide 38: Beacons
Source: NASA
Infrastructure-based

## Slide 39: Ultrasound
Ultrasound transceivers
  Active Bat, AT&T Labs Cambridge
  Cricket system, MIT
Smartphone-based (integrated mic)
  Acoustic Location Processing System (ALPS), CMU: 31cm avg. positioning error (winners of Microsoft Contest 2015)
Infrastructure-based

## Slide 40: LED Visible Light
LED light bulbs can switch on/off at high frequency (not visible to human eye) transmitting their ID.
  Light sensor decodes light signal intensities and estimates distances from LEDs to get user location
  Academic: Epsilon (Microsoft Research)
  Industrial: ByteLight.com
  Similar ideas for Data Transm (LiFi) – Gbps already!
L. Li et al., "Epsilon: A Visible Light Based Positioning System", 11th USENIX Symposium on Networked Systems Design and Implementation (NSDI), 2014, pp. 331-343.
Infrastructure-based

## Slide 41: Ultra Wide Band (UWB)
Measures the time (nanosec) it takes for brief bursts of radio energy (pulses) to travel between radios using a large portion of the radio spectrum.
  Pros: Accuracy (Decawave reports 10cm accuracy!)
  Cons: Short range, computational cost, expensive equipment [Zebra demo kit costs $12,000 (2014)]
Driven by several players
  Ubisense (UK), Decawave (IE), Nanotron (GE), Time Domain (US), Zebra (US)
Infrastructure-based

## Slide 42: IIN Taxonomy
Infrastructure-based

## Slide 43: Industrial Solutions
Ekahau RTLS: WiFi/RFID tags, Healthcare, 300+hospitals
  Asset tracking, ​staff safety & workflow optimization, patient safety & throughput, ​temperature monitoring. [ Active-RFID-over-WiFi ]
Aislelabs: WiFi/iBeacon, Cloud-based retail analytics
  Customer behavior, personalized marketing, enterprise mobile wallet, indoor navigation, geofencing, in-store promotions [ BLE ]
Infrastructure-based

## Slide 44: Beacon (Applications)
Infrastructure-based
Shopping Analytics with Aislelabs

## Slide 45: Tutorial Outline
Introduction
Location
Modeling
Crowdsourcing
Privacy
Open Challenges

## Slide 46: Modeling
Indoor spaces exhibit complex topologies. They are composed of entities that are unique to indoor settings:
  e.g., rooms and hallways that are connected by doors.
  Conventional Euclidean distances are inapplicable in indoor space, e.g., NN of p1 is p2 not p3.
Jensen et. al. 2010

## Slide 47: Modeling
Geometric Model: uses points in N-dimensional space, allowing the calculation of Lp-norm distances.
Symbolic Model: uses reference points (e.g., rooms) to establish a structure for distance computation.
  Graph-based model for indoor G(V,E), V={rooms} E={doors,corridors,stairs,elevators} - Becker 2005.
  This allows direct usage of graph algorithms (shortest path, connectivity, traversals, etc.)
To provide spatial queries, we additionally need to a complementary geometric extend to V.

## Slide 48: Modeling
Source: NASA
Technology roadmap is towards indoor GIS integration
  GeoJson.org (not specifically for indoor)
  IndoorGML.net

## Slide 49: GeoJson
Source: NASA
GeoJSON is a format for encoding a variety of geographic data structures (not only indoor)
  Not a formal GIS standard (i.e., OGC standard)
Convenient for Web 2.0 APIs
  Support: Micello Web Maps
Supports multiple geometry types
  Point, LineString, Polygon,
  MultiPoint, MultiLineString, and MultiPolygon

## Slide 50: IndoorGML
Source: NASA
Standard supported by Open Geospatial Consortium (OGC)
  Defined as an application schema of OGC Geographic Markup Language (GML) 3.2.1.
IndoorOSM (another older effort by Open Street Map) is deprecated

## Slide 51: IndoorGML – How It Works
Source: NASA

## Slide 52
Modeling in Anyplace
Demo
Multi-layered space (sensor + semantics)

## Slide 53: i-locate EU Project
Source: NASA
G. Conti, Keynote at International Conference on Indoor Positioning and Indoor Navigation (IPIN), Busan, S. Korea, 2014
Indoor counterpart to OSM

## Slide 54: i-locate Open Geodata Project
Source: NASA
Indoor/outdoor location and asset management through open geodata (EU ICT 2014-2016)
Main objectives
  Create a public geoportal for open indoor Geographical Information
  Extend current open standards (OSM) to support indoor and outdoor LBS
  Develop an open source “toolkit” for indoor and outdoor LBS
http://www.i-locate.eu/

## Slide 55: IIN Taxonomy

## Slide 56: Industrial Solutions
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Mazemap: Service for indoor maps (Needs Cisco CMX)
  Universities, hospitals, conference venues and shopping malls
  Timetable, mobile app, SMS notification, reserve room integration
Micello: Indoor maps,15,000+ venues, 50,000+ buildings
  Map integration, 3rd party navigation engine, multiple data formats
  49 USD / building / month (Jun. 2015)

## Slide 57: Google Indoor
Free to enrich Google Maps
Not clear how mapping is priortized by Google
No control over model
No fine location
Anyplace works over Google Indoor as a Map Layer!

## Slide 58: Tutorial Outline
Introduction
Location
Modeling
Crowdsourcing
Privacy
Open Challenges

## Slide 59: Crowdsourcing
A smartphone crowd is constantly moving and sensing providing large amounts of sensor data enabling new applications
  “Crowdsourcing with Smartphones”, Georgios Chatzimiloudis, Andreas Konstantinidis, Christos Laoudias, Demetrios Zeinalipour-Yazti, IEEE Internet Computing, Special Issue: Sep/Oct 2012 - Crowdsourcing, May 2012. IEEE Press, Volume 16, pp. 36-44, 2012.

## Slide 60: Non-Participatory vs. Participatory
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Non-participatory systems: Paid professionals (Micello, Mazemap, Ekahau) or a team of trained volunteers (KAILOS project) undertake the data collection
Participatory systems: employ feedback from regular users to expand a core signal database created by trained contributors or regular users.

## Slide 61: Non-Participatory
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Non-participatory systems
Pros
  Collected data span the entire area (no black holes)
  Sufficient data to build reliable signal maps
Cons
  Laborious and time consuming:
    15 collectors for 2 weeks, 200,000 WiFi readings at 10,000 locations to cover 450,000 m2 shopping mall in S. Korea
  High costs
    0.17 USD per m2 in Mazemap (only the map – no signals)
    Older versions of Ekahau system installation costed $10,000 for a large office building (no maintenance included)
Non-Participatory

## Slide 62: KAILOS Academic Project
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
KAIST(S. Korea) http://kailos.io
Non-Participatory

## Slide 63: Active Campus (UCSD)
Source: NASA
Dating back to 2004 …
When a user’s location is displayed incorrectly, the user clicks on the map to correct location
Participatory

## Slide 64: Place Lab (Intel)
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
http://www.placelab.org
Participatory
Microsoft Research
  Among the first systems in 2005 (IEEE Pervasive) promoting user collaboration.
AP

## Slide 65: Zee (Microsoft Research)
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Zero-effort fingerprint collection
  WiFi Data are crowdsourced without explicit user participation (app runs in the background)
  Leverages smartphone IMU sensors (direction, step counting, stride length estimation)
Participatory
Rai et. al., “Zee: zero-effort crowdsourcing for indoor localization”. In ACM Mobicom '12

## Slide 66: SmartCampusAAU (Aalborg)
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Open-source system
Features both terminal and network-based localization to support all three major mobile OS platforms (Android, iOS, Windows)
Participatory

## Slide 67: IIN Taxonomy

## Slide 68: Tutorial Outline
Introduction
Location
Modeling
Crowdsourcing
Privacy
Open Challenges

## Slide 69: Location Privacy Threat
Location tracking is unethical and can even be illegal if it is carried out without the explicit user consent.
Imminent privacy threat, with greater impact that other location tracking concerns, as it can occur at a very fine granularity. It reveals:
  The stores / products of interest in a mall.
  The book shelves of interest in a library
  Artifacts observed in a museum, etc.

## Slide 70: Location Privacy
Users don’t know where IPS operate their data and whether these conform or not to latest legislative efforts and reforms:
  EU Data Protection Directive
  US White House consumer Privacy Bill of Rights
  US-EU Safe Harbor guidelines
  US Do-Not-Track Online Act
IPS might become attractive targets for hackers, aiming to steal location data and carry out illegal acts (e.g., break into houses).
IPS should be considered as fundamentally untrusted entities, so we aim to devise techniques that are exploit IPS utility with controllable privacy to the user.

## Slide 71: Privacy vs No Privacy
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Network-based geolocation systems can always “know” the location of users while serving them.
Privacy (terminal-based) solutions
  Calculate location directly at the user-carried device
  Use sensor readings produced or downloaded locally
No Privacy (network-based) solutions
  Rely continuously on the service for user geolocation
  Use location-dependent observations
    monitored by the network infrastructure
    collected by mobile devices (terminal-assisted mode)

## Slide 72: Location Privacy
RadioMap Service
...
I can see these Reference Points, where am I?
(x,y)!
User u
Privacy-Preserving Indoor Localization on Smartphones, Andreas Konstantinidis, Paschalis Mpeis, Demetrios Zeinalipour-Yazti and Yannis Theodoridis, in IEEE TKDE’15
Towards planet-scale localization on smartphones with a partial radiomap", A. Konstantinidis, G. Chatzimilioudis, C. Laoudias, S. Nicolaou and D. Zeinalipour-Yazti. In ACM HotPlanet'12, in conjunction with ACM MobiSys '12, ACM, Pages: 9--14, 2012.

## Slide 73: Temporal Vector Map (TVM)
RadioMap (server-side)
WiFi
WiFi
WiFi
...
Bloom Filter (u's APs)
K=3 Positions
User u
Set Membership Queries
Contains false positives
Doesn’t contain false negatives

## Slide 74: Tutorial Outline
Introduction
Location
Modeling
Crowdsourcing
Privacy
Open Challenges

## Slide 75: Localization Challenges
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Fuse multi-modal location-dependent sensing data
  coming from highly diverse, low-cost and error-prone smartphone sensors
Provide seamless indoor/outdoor transition
  switch from GPS geolocation in open sky to indoor solutions when the quality of satellite signals degrades
  transparent cross-floor movement
    timely detecting elevation changes
    identify the correct floor and display the corresponding map
Intelligent switching among indoor systems
  Ubiquity of indoor solutions will lead to overlaps
  Diverse application requirements: availability, power consumption, accuracy, precision.

## Slide 76
Localization Challenges
Problem: When a users moves inside an indoor space connectivity might be lost
  intermittent connectivity.
  WiFi AP out of range.
As such, continuous localization with input from the IPS is a challenging task.
Preloading the complete building or area map (like in GPS) is difficult due to scale and due to frequently updated data (by crowdsourcers)

## Slide 77: Intermittent Connectivity
IIN Service
Where-am-I?
 Intermittent Connectivity
Where-am-I?
Where-am-I?
No Navigation
Time
X

## Slide 78: PreLoc Navigation
IIN Service
Prefetch K RM rows
 Intermittent Connectivity
Prefetch K RM rows
Time
Prefetch K RM rows
X
Localize from Cache

## Slide 79: Modeling Challenges
Basic Operation on Smartphone Power(mW=mJ/s)
CPU Minimal use (just OS running) 35mW
CPU Standard use (light processing) 175mW
CPU Peak (heavy processing) 469mW
WiFi Idle (Connected) 34mW
WiFi Localization (avg/minute) 125mW
WiFi Peak (Uplink 123Kbps, -58dBm) 400mW
3G Localization (avg/minute) 300mW
3G Busy 900mW
GPS On (steady) 275mW
OLED Economy Mode 300mW
OLED Full Brightness 676mW
Source: NASA
Advanced graph automation tasks
  Check the indoor model (graph connectivity, automatically connect overlapping stairs and elevators)
Algorithms to handle click-streams of error reports and dispute resolution techniques
  Majority voting algorithms
Integration to open standards
  Boost openness and data portability among different geolocation services
  Facilitate easier data entry

## Slide 80: Crowdsourcing Challenges
Logging “big” quantities of RSSI fingerprints in the cloud, calls for scalable processing architectures.
  Historic RSSI for buildings (Offline Data)
  Online RSSI that arrive from Crowdsourcers (Online Data)
Apache Hadoop is nowadays widely endorsed by the industry and academia for offline processing of data using the Map/Reduce programming paradigm.
Newer trends provide:
  performance abstractions.
  In-Memory processing concepts

## Slide 81
Massively process RSS log traces to generate a valuable Radiomap
Processing current logs in Anyplace for a single building takes several minutes!
Challenges in MapReduce:
  Collect Statistics (count, RSSI mean and standard deviation)
  Remove Outlier Values.
  Handle Diversity Issues
Crowdsourcing Challenges

## Slide 82
Quality: Unreliable Crowdsourcers, Multi-device Issues, Hardware Outliers, Temporal Decay, etc.
  Remark: There is a Linear Relation between RSS values of devices.
  Challenge: Can we exploit this to align reported RSS values?
"Crowdsourced Indoor Localization for Diverse Devices through Radiomap Fusion", C. Laoudias, D. Zeinalipour-Yazti and C. G. Panayiotou, "Proceedings of the 4th Intl. Conference on Indoor Positioning and Indoor Navigation" (IPIN '13), Montbeliard-Belfort France, 2013.
Crowdsourcing Challenges

## Slide 83: Mobile Data Management in Indoor Spaces
Christos Laoudias§and Demetrios Zeinalipour-Yazti∗
Advanced Seminar at 16th IEEE Int. Conference on Mobile Data Management (MDM’15), Pittsburgh, PA, USA, June 17, 2015
http://goo.gl/70JV4q
Thank You! Questions?
Contact: laoudias@ucy.ac.cy; dzeina@cs.ucy.ac.cy