## Slide 1: An IoT Data System for Solar Self-Consumption Soteris Constantinou 1, Nicolas Polycarpou 1, Constantinos Costa 2,1,4, Andreas Konstantinidis 3,1, Panos K. Chrysanthis 4,1, Demetrios Zeinalipour-Yazti 1 1 University of Cyprus, Cyprus | 2 Rinnoco Ltd, Cyprus | 3 Frederick University, Cyprus | 4 University of Pittsburgh, USA
Green Planning refers to computational approaches that aim to make rapid progress towards sustainability through load shifting considering peak demand reduction.
Benefits:
  Self-consumption is more beneficial than energy storage in Batteries!
     17% of the energy is lost in AC/DC conversion and heat dissipation
  Self-consumption can make houses 70% CO2 neutral w/out batteries!
  Load shifting to avoid peak-demand times (considers solar production)
Observations
  Residential solar system: ~10kWp
  10 hours of solar radiation x 60 minutes => 600 time slots (x-axis)
  Approximate the curve by 2 triangles of size (3K cells to plan daily): [height = 10kWp / 1kW = 10] x [base = 5x60 = 300 minutes]
Challenge: How to intelligently schedule (i.e., fill the cells) with device operations considering that energy-demanding devices operate at various load levels?
The global Home Energy Management Systems (HEMS) market
  increased from USD 864.2 million in 2015 to USD 3.15 billion by 2022
European’s Commission calls for a climate-neutral Europe by 2050
Internet-connected smart devices worldwide
  - 100B connected devices by 2030 - 30.9B units by 2025
GreenCap (best performance): very high user comfort ≈ 92%, an impressive self-consumption ≈ 52%, and imported energy ≈ 48%
Brute Force: best self-consumption ≈ 67% and imported energy ≈ 32% retrieved, however user comfort ranges at only ≈ 40%
In countries with high kg CO2 per kWh factor, GreenCap can reduce up to ≈ 40% of the carbon dioxide emissions
GreenCap’s execution (90 secs) is ≈16.5 times faster than Brute Force approach
[1] "An IoT Data System for Solar Self-Consumption", Soteris Constantinou, Nicolas Polycarpou, Constantinos Costa, Andreas Konstantinidis, Panos K. Chrysanthis, Demetrios Zeinalipour-Yazti, The 24th IEEE International Conference on Mobile Data Management (MDM'23), 2023.
[2] "Green Planning of IoT Home Automation Workflows in Smart Buildings", Soteris Constantinou, Andreas Konstantinides, Panos K. Chrysanthis and Demetrios Zeinalipour-Yazti, ACM Transactions on Internet of Things (TIOT'22), Vol. 3, Iss. 4, pp. 1--30,, 2022.
[3] "The IoT Meta-Control Firewall", Soteris Constantinou, Andreas Konstantinidis, Demetrios Zeinalipour-Yazti, Panos K. Chrysanthis, 37th IEEE Intl. Conference on Data Engineering (ICDE'21), pp. 2523-2534, 2021.
Motivation
Green Planning
GreenCap: Algorithm
GreenCap: System Architecture
GreenCap Performance
Evolutionary algorithm: generates high-quality solution to a particular search problem by relying on bioinspired operators
Each IoT device is represented with a chromosome (i.e., IoT device ON = 1, IoT device OFF = 0)
Improves users’ comfort and provide high convergence by reducing the likelihood of trapping in local optima
Input parameters: - Residential Consumption Record (RCR) - Preference Rules (PR) user-configured - Weather Forecast
https://greencap.cs.ucy.ac.cy/
Contact: dmsl@ucy.ac.cy
https://dmsl.cs.ucy.ac.cy/
(Local) Control Unit: direct communication with the IoT devices
OpenHAB/Domoticz: residential management application
GUI: enable users to configure custom rules
GreenCap Controller: energy management framework
GreenCap: User Interface
anyplace.cs.ucy.ac.cy
Records OpenHAB’s smart device measurements on local storage
Configures various meta-rules related to the operation time of IoT
Gets an efficient execution considering user satisfaction
Demonstrates results on user friendly graphs